Changing the Disc in the Background

Some developers have asked for a way to make DRM-600 series drives 
change discs without requiring the normal 5-7 second wait.  This 
can be done using Pioneer's CDP (Character Device Player) device 
driver.  CDP is a character device driver that's built into the 
DRD6XX.SYS drivers.  It is enabled with "/C:CDP" in the CONFIG.SYS 
device line.

CDP allows the use of Pioneer's mnemonic commands.  Normally, CDP 
waits for the return from the command, but this can be disabled by 
prefixing the command with "|n"  From DOS, the command
echo 2ZS > cdp
will cause a change to disc 2 (as seen on the magazine).  It will 
wait for the return from the drive.  Under DOS, there seems to be 
no way to prevent the "|" from being interpreted as a pipe.  You 
can, however, copy a file with the command to CDP.

Here's a sample C program:

#include <stdio.h>

main()
{
	FILE *handle;

	if ((handle = fopen("cdp", "r+w")) == NULL ){
		printf("\n Could not open cdp");
		exit(1);
		}

	if (setvbuf(handle,NULL,_IONBF,0)){     /* No buffering */
		printf("\setvbuf failed");
		}

	fprintf(handle, "|n1zs\r");
	printf("\n1zs issued");
	getch();

	fprintf(handle, "|n2zs\r");
	printf("\n2zs issued");
	getch();

	fprintf(handle, "|n3zs\r");
	printf("\n3zs issued");
	getch();

	fprintf(handle, "|n4zs\r");
	printf("\n4zs issued");
	getch();



	fprintf(handle, "|n5zs\r");
	printf("\n5zs issued");
	getch();

	fclose(handle);
}

NOTE:  Each command must be terminated with a carriage return.

Writing a new command before an old command has begun execution 
will overwrite the old command.  You can see this if you remove 
the getch() calls above.  In this case, the "1zs" will begin 
execution.  Then the "2ZS" will be overwritten by "3ZS", "3ZS" by 
"4ZS", and "4ZS" will be overwritten by "5ZS".  So you will see 
the drive pull in disc 1, and then disc 5.

The CDP functionality is also available through the Pioneer-unique 
WRITE CDP and READ CDP SCSI commands.